## Slide 1
WMO, 1978: Compendium of Meteorology; Vol I, Part 3 – Synoptic Meteorolgy
Prepared by Defant with Mörth
Disponível na biblioteca do IAG
Cartas meteorológicas e dados sinóticos (plotagens, interpretação e análise) SYNOP
Notes: 14/04/09 – 12z

## Slide 2: Objetivo
Decodificar o código SYNOP
Plotar dados numa carta de superfície

## Slide 3: Dados observacionais
Dados de superfície
Dados de altitude

## Slide 4: Dados de superfície
Estações meteorológicas
Observação dos seguintes elementos (WMO):
  Tempo presente
  Tempo passado
  Velocidade e direção do vento
  Tipo e quantidade de nuvens
  Visibilidade
  Temperatura
  Umidade
  Pressão

## Slide 5: Estação meteorológica de superfície
Adicionalmente:
  Tendência de pressão
  Temperaturas extremas
  Quantidade de precipitação
  Estado da superfície
  Direção do movimento de nuvens
  Fenômenos especiais

## Slide 6: Horários de observação
Horários sinóticos principais:
  0000 e 1200GMT
  0600 e 1800GMT
Horários intermediários:
  0300, 0900, 1500 e 2100GMT
Recomendação da OMM: observação da pressão deve ocorrer exatamente no horário sinótico; outros elementos num intervalo de 10 minutos antes do horário sinótico.

## Slide 7: Dados de altitude
Pressão, temperatura e umidade
Velocidade e direção do vento
Radiosondagem: velocidade de ascensão ~constante (300m.min-1)
Horários: 0000 e 1200GMT
Início da sondagem normalmente ocorre uma hora antes do horário sinótico. Intervalo de tempo necessário para um balão subir do nível do mar a 100hPa (~16km).

## Slide 8: Dados de altitude
Elementos a serem reportados:
Temperatura, depressão do ponto de orvalho (T-Td) e altura geopotencial nos níveis padrões de pressão: 1000, 850, 700, 500, 400, 300, 250, 150 e 100hPa, na troposfera, e 70, 50, 30, 20 e 10hPa na estratosfera.
Pontos especiais (onde tais elementos mostrem descontinuidades significativas)

## Slide 9: Altura geopotencial
Geopotencial:
Altura geopotencial:
Eq. hipsométrica:
Aproximação:
http://www.ofcm.gov/fmh3/pdf/12-app-d.pdf

## Slide 10: Outras fontes
Estações oceanográficas
Satélites meteorológicos
Balões
Aviões

## Slide 11: Rede sinótica básica de superfície
Região I – África
Região II – Ásia
Região III – América do Sul
Região IV – América do Norte e Central
Região V – Sudoeste do Pacífico
Região VI – Europa
Antártica

## Slide 12: Número das estações http://www.wetterzentrale.de/klima/stnlst.html
NUMBER CALL NAME + COUNTRY/STATE LAT LON ELEV (METERS)
010010 ENJA JAN MAYEN(NOR-NAVY) NO 7056N 00840W 0009
020120 RITSEM SN 6744N 01728E 0523
028010 KILPISJARVI FI 6903N 02047E 0476
030010 MUCKLE FLUGGA (LH) UK 6051N 00053W 0053
070020 BOULOGNE FR 5044N 00136E 0074
080010 LA CORUNA CITY SP 4322N 00825W 0067
085350 LISBON PO 3843N 00909W 0095
103810 BERLIN/DAHLEM DL 5228N 01318E 0058
115180 LKPR PRAGUE/RUZYNE CZ 5006N 01417E 0365
150000 BOGUS ROMANIAN RO 0000N 00000E 0261
161303 LIMP PARMA & IY 4449N 01018E 0050
167010 ATHENS/FILADELFIA GR 3803N 02340E 0138
716270 YUL MONTREAL/DORVAL CN 4528N 07345W 0036
725030 LGA NEW YORK/LA GUARDIA NY 4046N 07354W 0009
766793 MMMX MEXICO CITY/LICENCI MX 1926N 09906W 2238
820140 NORMANDIA BZ 0330N 06010W 0700
820170 SBOI OIAPOQUE BZ 0350N 05150W 0039
carta_09041418\estacoes synop texto.txt

## Slide 13: Estações Brasil
82: estações ao norte de 10oS
83: estações a sul de 10oS
São Paulo:
  837753 SBGR GUARULHOS (CIV/MIL) BZ 2326S 04628W 0750
  837790 SBMT MARTE (CIV/MIL) BZ 2331S 04638W 0722
  837800 SBSP SAO PAULO/CONGONHAS BZ 2337S 04639W 0803
  837810 SAO PAULO BZ 2330S 04637W 0792
  83004 IAG

## Slide 14: Estações América do Sul
802220 SKBO BOGOTA/ELDORADO CO 0442N 07408W 2548
804150 SVMI CARACAS/S. BOLIVAR VN 1036N 06659W 0048
810020 SYTM GEORGETOWN/TIMEHRI GY 0630N 05815W 0030
812250 SMZY ZANDERY/PARAMARIBO SM 0527N 05512W 0015
814050 SOCA CAYENNE/ROCHAMBEAU FG 0450N 05222W 0009

## Slide 15: América do Sul
840710 SEQU QUITO/MARISCAL SUC& EQ 0009S 07829W 2812
846280 SPIM LIMA/JORGE CHAVEZ PR 1200S 07707W 0013
852010 SLLP LA PAZ/JFK INTL BO 1631S 06811W 4014
855740 SCEL PUDAHUEL/ARTURO MER CH 3323S 07047W 0476 Santiago
862180 SGAS ASUNCION/SILVIO PET PY 2516S 05738W 0101
865800 SUMU CARRASCO (CIV/MIL) UY 3450S 05600W 0032 Montevideo
875760 SAEZ BUENOS AIRES/EZEIZA AG 3449S 05832W 0020
888910 SFAL STANLEY AIRPORT FK 5141S 05746W 0023

## Slide 16
80
81
82
83
84
85
86
87
88

## Slide 17: Código SYNOP
“Surface Synoptic Observations”: SYNOP Data Format (FM-12)
Surface Synoptic Observations
Table of Contents
Surface Observations
  000 Group - Identification and Location
  111 Group - Land Observations
  222 Group - Sea Surface Observations
  333 Group - Climatological Data
Arquivo: LandSynopticCode.pdf

## Slide 18: SYNOP
Syntax
IIiii or IIIII YYGGi 99LLL QLLLL iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
222Dv 0sTTT 1PPHH 2PPHH 3dddd 4PPHH 5PPHH 6IEER 70HHH 8aTTT 333 0.... 1sTTT 2sTTT 3Ejjj 4Esss 5jjjj jjjjj 6RRRt 7RRRR 8Nchh 9SSss

## Slide 19: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 20: Estações “terrestres” Arquivo SYNOP do MASTER
IIiii iihVV Nddff 00fff 1sTTT 2sTTT 3PPPP 4PPPP 5appp 6RRRt 7wwWW 8NCCC 9GGgg
IIiii – no. da estação
iR -- Precipitation indicator
ix -- Station type and present and past weather indicator
h -- Cloud base of lowest cloud seen (meters above ground)
VV -- Visibility

## Slide 24: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 25: IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N -- Total cloud cover
dd -- wind direction in 10s of degrees ff -- wind speed in units determined by wind type indicator (see above)
00fff (optional) fff -- wind speed if value greater than 100

## Slide 28: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 29: IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
1sTTT -- Temperature s -- sign of temperature (0=positive, 1=negative) TTT -- Temperature in .1 C
2sTTT -- Dewpoint s -- sign of temperature (0=positive, 1=negative, 9 = RH) TTT -- Dewpoint temperature in .1 C (if sign is 9, TTT is relative humidity)

## Slide 30: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 31: IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
3P0P0P0P0-- Station pressure in 0.1 mb (thousandths digit omitted, last digit can be slash, then pressure in full mb)
4PPPP -- Sea level pressure in 0.1 mb (thousandths digit omitted, last digit can be slash, then pressure in full mb)
4ahhh -- Geopotential of nearest mandatory pressure level (use for high altitude stations where sea level pressure reduction is not accurate) a -- mandatory pressure level
hhh -- geopotential height omitting thousandths digit

## Slide 33: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 34
5appp -- Pressure tendency over 3 hours a -- characteristics of pressure tendency ppp -- 3 hour pressure change in 0.1 mb

## Slide 35: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 36
6RRRt -- Liquid precipitation RRR -- Precipitation amount in mm
t -- Duration over which precipitation amount measured

## Slide 37
7wwWW -- Present and past weather ww -- Present weather
W1 -- Past weather (type 1) W2 -- Past weather (type 2)

## Slide 38: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff 00fff 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 39
8NHCCC -- Cloud type information NH -- Amount of low clouds covering sky, if no low clouds, the amount of the middle clouds CL -- Low cloud type
CM -- Middle cloud type
CH -- High cloud type
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww

## Slide 40: 333 Group - Section 3 contains information that is needed within a particular WMO region, or a portion of a region – Brasil – Grupo III
0.... -- Regionally developed data
1sTTT -- Maximum temperature over previous 24 hours s -- sign of temperature (0=positive, 1=negative) TTT -- Temperature in .1 C
2sTTT -- Minimum temperature over previous 24 hours s -- sign of temperature (0=positive, 1=negative) TTT -- Temperature in .1 C
3Ejjj -- Regionally developed data
4Esss -- Snow depth E -- State of ground with snow cover
http://weather.unisys.com/wxp/Appendices/Formats/SYNOP.html#333

## Slide 41: 333 Group - Special / Climatological Data
sss -- snow depth in cm
5jjjj jjjjj -- Additional information (can be multiple groups)
6RRRt -- Liquid precipitation RRR -- Precipitation amount in mm
t -- Duration over which precipitation amount measured (para t=4, período = 24 horas)
7RRRR -- 24 hour precipitation in mm
8NChh -- Cloud layer data N -- cloud coverage of layer C -- genus of cloud
hh -- height of cloud base
9SSss -- Supplementary information

## Slide 42: Plotando synop
Exemplo: Grupo 111 – SYNOP – Estação continental
IIiii iRiXhVV Nddff (00fff) 1sTTT 2sTdTdTd 3P0P0P0P0 4PPPP 5appp 6RRRt 7wwW1W2 8NhCLCMCH 9GGgg
N
CH
CM PPP
ppp a
W t
RRR
CL Nh
TT
TdTd
VV ww